## Slide 1: 8086 Introduction
By
G HARISH BABU M.Tech, [ Ph.D ]
Asst Professor
Dept of ECE
CVR COLLEGE OF ENGINEERING

## Slide 2: Register organization
8086 has a powerful set of registers containing general purpose and special purpose registers.
All the registers of 8086 are 16-bit registers
The general purpose registers, can be used either 8-bit registers or 16-bit registers.
The general purpose registers are either used for holding the data, variables and intermediate results temporarily or for other purpose like counter or for storing offset address for some particular addressing modes etc.
The special purpose registers are used as segment registers, pointers, index registers or as offset storage registers for particular addressing modes

## Slide 3
AH | AL
BH | BL
CH | CL
DH | DL
CS
SS
DS
ES
SP
BP
SI
DI
IP
FLAG/PSW
GENERAL DATA REGISTERS
SEGMENT REGISTERS
POINTER & INDEX REGISTERS

## Slide 4: ARCHITECTURE OF 8086

## Slide 7: BIU (Bus interface unit)
Functions of Bus interface unit
It sends address of the memory or I/o.
It fetches instruction from memory.
It reads data from port/memory.
It writes data into port/memory.
It supports instruction queuing.
It provides the address relocation facility.

## Slide 8
30007 h | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
30006 h | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
30005 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30004 h | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
30003 h | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
30002 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30001 h | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
30000 h | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
ES
CS
SS
DS
IP
MEMORY
6
5
4
3
2
1
physical Address =segment address *10h + offset address
Ex:-CS=3000h , IP=0001h
PA=3000h*10h+0000h
=30000h+0000h
=30000h
INCREMENT IP
30000H
00110100

## Slide 9
30007 h | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
30006 h | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
30005 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30004 h | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
30003 h | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
30002 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30001 h | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
30000 h | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
ES
CS
SS
DS
IP
MEMORY
6
5
4
3
2
1
physical Address =segment address *10h + offset address
Ex:-CS=3000h , IP=0001h
PA=3000h*10h+0001h
=30000h+0001h
=30001h
INCREMENT IP
30001H
00010010

## Slide 10
30007 h | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
30006 h | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
30005 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30004 h | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
30003 h | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
30002 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30001 h | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
30000 h | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
ES
CS
SS
DS
IP
MEMORY
6
5
4
3
2
1
physical Address =segment address *10h + offset address
Ex:-CS=3000h , IP=0002h
PA=3000h*10h+0002h
=30000h+0002h
=30002h
INCREMENT IP
30002H
01010101

## Slide 11
30007 h | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
30006 h | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
30005 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30004 h | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
30003 h | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
30002 h | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
30001 h | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
30000 h | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
ES
CS
SS
DS
IP
MEMORY
6
5
4
3
2
1
physical Address =segment address *10h + offset address
Ex:-CS=3000h , IP=0003h
PA=3000h*10h+0003h
=30000h+0003h
=30003h
INCREMENT IP
30003H
00010010

## Slide 12: EU (Execution Unit)
Control circuitry.
Instruction Decoder.
ALU.
Flag register.
General purpose registers.
Pointer and index registers.

## Slide 14: Flag register
The 8086 has 16 bit Flag register.
It is divided into two parts
  Condition code or status flags.
  Machine control flags.
  (D,I,T)
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
X | X | X | X | O | D | I | T | S | Z | X | Ac | X | P | X | Cy

## Slide 15: Memory Segmentation
The memory in an 8086/8088 based system is organised as segmented memory.
The complete physical memory (1MB) is divided into a 16 logical segments.
Each segment is 64Kb size.
The 16 bit contents of the segment register actually point to the starting location of a particular segment.
To address a specific memory location within a segment we need an offset address.
The offset address is also 16 bit long so that the maximum offset value can be FFFFh

## Slide 17
FFFF 64KB 0000
FFFF 64KB 0000
CS2
CS1
Offset IP1
Offset IP2
00000H
FFFFFH
2500H
1000H
SEGMENT 2
SEGMENT 1
FFFF 64KB
FFFF 0000,1A01
1A00 64KB 0000
CS2
CS1
Offset IP1
Offset IP2
0000H
FFFFFH
SEGMENT
NON OVERLAPPING SEGMENTS
OVERLAPPING SEGMENTS
OVERLAP
Overlapped segmented area

## Slide 18: Advantages
Allows the memory capacity to 1MBytes although the actual address to be handled are 16 bit size.
Allows the placing of code , data and stack portions of the same program in different parts (segments) of memory , for data and code protection.
Permits a program and/or its data to be put into different areas of memory each time the program is executed i.e provision for relocation is done.

## Slide 19: Memory segmentation
Rules for memory segmentation
1.The four segments can overlap for small programs. In a minimum system all four segments can start at the address 00000h.
2.The segment can begin/start at any memory address which is divisible by 16.