## Slide 1: Digital Image fundamentals

## Slide 2
Digital Image
— a two-dimensional function
x and y are spatial coordinates
The amplitude of f is called intensity or gray level at the point (x, y)
Digital Image Processing
— process digital images by means of computer, it covers low-, mid-, and high-level processes
low-level: inputs and outputs are images
mid-level: outputs are attributes extracted from input images
high-level: an ensemble of recognition of individual objects
Pixel
— the elements of a digital image

## Slide 3: Sources for Images
Electromagnetic (EM) energy spectrum
Acoustic
Ultrasonic
Electronic
Synthetic images produced by computer

## Slide 4
What is an image?
0
255
8 bits/pixel

## Slide 5: How Images are Represented
Bitmap images (Dots used to draw the image)
  Monochrome images
  8 bit grey scale images
  24 bit colour
  Colour lookup tables
Vector Graphics (Line art)
  Rasterisation
Two key concepts
  Image resolution
  Colour resolution

## Slide 6: Fundamental Steps in DIP
Improving the appearance
Result is more suitable than the original
Partition an image into its constituent parts or objects
Represent image for computer processing
Extracting image components

## Slide 7: Image Acquisition
Transform illumination energy into digital images

## Slide 8: Image Acquisition Using a Single Sensor

## Slide 9: Image Acquisition Using Sensor Strips

## Slide 10: Image Acquisition Process

## Slide 11: A Simple Image Formation Model

## Slide 12: Some Typical Ranges of illumination
Illumination
  Lumen — A unit of light flow or luminous flux
  Lumen per square meter (lm/m2) — The metric unit of measure for illuminance of a surface
  On a clear day, the sun may produce in excess of 90,000 lm/m2 of illumination on the surface of the Earth
  On a cloudy day, the sun may produce less than 10,000 lm/m2 of illumination on the surface of the Earth
  On a clear evening, the moon yields about 0.1 lm/m2 of illumination
  The typical illumination level in a commercial office is about 1000 lm/m2

## Slide 13: Some Typical Ranges of Reflectance
Reflectance
  0.01 for black velvet
  0.65 for stainless steel
  0.80 for flat-white wall paint
  0.90 for silver-plated metal
  0.93 for snow

## Slide 14: Image Quantization
Sampling: measure the value of an image at a finite number of points.
Quantization: represent measured value (i.e., voltage) at the sampled point by an integer.

## Slide 15: Image Sampling and Quantization
Digitizing the coordinate values
Digitizing the amplitude values

## Slide 16
Image Sampling – Example
Original image Sampled by a factor of 2
Sampled by a factor of 4 Sampled by a factor of 8

## Slide 17: Image Sampling and Quantization

## Slide 18: Image Quantization
256 gray levels (8bits/pixel) 32 gray levels (5 bits/pixel) 16 gray levels (4 bits/pixel)
8 gray levels (3 bits/pixel) 4 gray levels (2 bits/pixel) 2 gray levels (1 bit/pixel)

## Slide 19: Image Quantization
8 Bit Grey Scale Images Vs Binary Image

## Slide 20: Representing Digital Images

## Slide 21: Representing Digital Images
The representation of an M×N numerical array as

## Slide 22: Representing Digital Images
The representation of an M×N numerical array as

## Slide 23: Representing Digital Images
The representation of an M×N numerical array in MATLAB

## Slide 24: Representing Digital Images
Discrete intensity interval [0, L-1], L=2k
The number b of bits required to store a M × N digitized image
b = M × N × k

## Slide 25: Representing Digital Images

## Slide 26: Spatial and Intensity Resolution
Spatial resolution
— A measure of the smallest discernible detail in an image
— stated with line pairs per unit distance, dots (pixels) per unit distance, dots per inch (dpi)
Intensity resolution
— The smallest discernible change in intensity level
— stated with 8 bits, 12 bits, 16 bits, etc.

## Slide 27: Spatial and Intensity Resolution

## Slide 28: Spatial and Intensity Resolution

## Slide 29: Color Images
Color images are comprised of three color channels – red, green, and, blue – which combine to create most of the colors we can see

## Slide 30: Color Images

## Slide 31: Color Images
This time a single pixel is made up of 3 bytes or 24 bits.

## Slide 32: Alternative Color Spaces
Various other color representations can be computed from RGB.
This can be done for:
  Decorrelating the color channels:
    principal components.
  Bringing color information to the fore:
    Hue, saturation and brightness.
  Perceptual uniformity:
    CIELuv, CIELab, …

## Slide 33: 8 bit Colour Images and Look up Tables
Draw three blue dots
Pixel | Red | Green | Blue
1 RGB(0,0,255) | 0 (1 byte) | 0 (1 byte) | 255 (1 byte)
2 RGB(0,0,255) | 0 (1 byte) | 0 (1 byte) | 255 (1 byte)
3 RGB(0,0,255) | 0 (1 byte) | 0 (1 byte) | 255 (1 byte)
4 RGB(0,0,255) | 0 (1 byte) | 0 (1 byte) | 255 (1 byte)
No of bytes = 12

## Slide 34: Processing Strategy
Red
Green
Blue
T-1
Processing
T
Red
Green
Blue

## Slide 35: Skin color
RGB
rg
r
g

## Slide 36: Skin detection
M. Jones and J. Rehg, Statistical Color Models with Application to Skin Detection, International Journal of Computer Vision, 2002

## Slide 37: Image file formats
Many image formats adhere to the simple model shown below (line by line, no breaks between lines).
The header contains at least the width and height of the image.
Most headers begin with a signature or “magic number”
(i.e., a short sequence of bytes for identifying the file format)

## Slide 38: Common image file formats
GIF (Graphic Interchange Format)
PNG (Portable Network Graphics)
JPEG (Joint Photographic Experts Group)
TIFF (Tagged Image File Format)
PGM (Portable Gray Map)
FITS (Flexible Image Transport System)

## Slide 39: PBM/PGM/PPM format
A popular format for grayscale images (8 bits/pixel)
Closely-related formats are:
  PBM (Portable Bitmap), for binary images (1 bit/pixel)
  PPM (Portable Pixelmap), for color images (24 bits/pixel)
        ASCII or binary (raw) storage

## Slide 40: Representing Digital Images
Digital images are composed of PIXELS (or picture elements)
  a natural image is typically represented by a continuous or analog signal (such as a photograph, video frame, etc.)
  Digitizing samples the natural image into discrete components

## Slide 41: Representing Digital Images
Digital images are composed of PIXELS (or picture elements)
  Each discrete sample is averaged to represent a uniform value for that area in the image
  PICTURE RESOLUTION is the number of pixels or samples used to represent the image

## Slide 42: Representing Digital Images
Digital images are composed of PIXELS (or picture elements)
  ASPECT RATIO expresses this resolution as the product of the no. of horizontal pixels by the no. of vertical pixels
  this image is square, 50 X 50
  sample ratios are 320 X 200 or 1.6:1, 640 X 480, 800 X 600, and 1024 X 768--all of which are 1.33:1

## Slide 43: Representing Digital Images
here is a (edited) digitized image with a resolution of 272 X 416
Picture resolution determines both the amount of detail as well as its storage requirements

## Slide 44: Representing Digital Images
notice more changes when the resolution is reduced (68 X 104)
Picture resolution determines both the amount of detail as well as its storage requirements

## Slide 45: Representing Digital Images
notice the changes when the resolution is reduced (136 X 208)
Picture resolution determines both the amount of detail as well as its storage requirements

## Slide 46: Image Size
“image size” refers to both
  Picture resolution
  Physical dimensions of the image
the physical dimensions of the image are determined by
  the number of pixels in the image (resolution) and
  the characteristics of the output device

## Slide 47: Image Size
Here are
  an image with a resolution of 300 X 300 at 72 dpi.
      And
  with a resolution of 300 X 300 at 300 dpi.

## Slide 48: Spatial Resolution
The spatial resolution of an image is determined by how sampling was carried out
Spatial resolution simply refers to the smallest discernible detail in an image
      Vision specialists will often talk about pixel size
      Graphic designers will talk about dots per inch (DPI)

## Slide 49: Spatial Resolution (cont…)

## Slide 50: Spatial Resolution (cont…)

## Slide 51: Spatial Resolution (cont…)

## Slide 52: Spatial Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 53: Spatial Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 54: Spatial Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 55: Spatial Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 56: Intensity Level Resolution
Intensity level resolution refers to the number of intensity levels used to represent the image
  The more intensity levels used, the finer the level of detail discernable in an image
  Intensity level resolution is usually given in terms of the number of bits used to store each intensity level
Number of Bits
Number of Intensity Levels
Examples
1
2
0, 1
2
4
00, 01, 10, 11
4
16
0000, 0101, 1111
8
256
00110011, 01010101
16
65,536
1010101010101010

## Slide 57: Intensity Level Resolution (cont…)
128 grey levels (7 bpp)
64 grey levels (6 bpp)
32 grey levels (5 bpp)
16 grey levels (4 bpp)
8 grey levels (3 bpp)
4 grey levels (2 bpp)
2 grey levels (1 bpp)
256 grey levels (8 bits per pixel)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 58: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 59: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 60: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 61: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 62: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 63: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 64: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 65: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 66: Saturation & Noise
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 67: Resolution: How Much Is Enough?
The big question with resolution is always how much is enough?
  This all depends on what is in the image and what you would like to do with it
  Key questions include
    Does the image look aesthetically pleasing?
    Can you see what you need to see within the image?

## Slide 68: Resolution: How Much Is Enough? (cont…)
The picture on the right is fine for counting the number of cars, but not for reading the number plate

## Slide 69: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)
Low Detail
Medium Detail
High Detail

## Slide 70: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 71: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 72: Intensity Level Resolution (cont…)
Images taken from Gonzalez & Woods, Digital Image Processing (2002)

## Slide 73: END